## Slide 1: NeuroDOT
Tutorial:
Image Reconstruction

## Slide 2: Diffuse Optical Tomography
In diffuse optical tomography (DOT), arrays of optical sources and detectors are used to perform functional neuroimaging experiments on task-based or resting state modes of human brain function.
Analyses are broken into several pipelines:
  B: modeling of the tissue shape, optical property distribution, and source/detector locations
  C: modeling of the light emission, diffusion, and detection through the head
  D: preprocessing of the raw source-detector measurements
  E: reconstruction and spectroscopy of the preprocessed data and light model into a functional neuroimaging volume
  F: post-processing analysis of these results.

## Slide 3: Image Reconstruction
This tutorial follows the NeuroDOT_ImageReconstruction_Script.m Matlab file which can be found in the Documentation/Scripts folder.
It expands on the full tutorial, NeuroDOT_Full_Processing_Script.m, and assumes the necessary sensitivity matrices are available
The tutorial will:
  Process source-detector measurements
  Perform image reconstruction using a light model sensitivity matrix A
  Visualize the reconstructed data
We will use data from a rotating-wedge retinotopy experiment
Start by loading this data set:
load('NeuroDOT_Data_Sample_CCW1.mat'); % data, info, flags

## Slide 4: Flow Chart for Pre-processing and Image Reconstruction
DOT Acquisition
Log-mean
Detect noisy channels
Band-pass filter
Superficial signal regression
Resample
Low-pass filter
Reconstruction
Spectroscopy
Spatial normalization
Light
Model

## Slide 5: Pre-processing
Pre-processing generally follows this pipeline:
  lmdata = logmean(data); % Logmean Light Levels
  info = FindGoodMeas(lmdata, info, 0.075); % Detect Noisy Channels
  lmdata = detrend_tts(lmdata); % Detrend Data
  lmdata = highpass(lmdata, .02, info.system.framerate); % HPF
  lmdata = lowpass(lmdata, 1, info.system.framerate); % LPF 1
  hem = gethem(lmdata, info); % Superficial Signal Regression
  [lmdata, ~] = regcorr(lmdata, info, hem);
  lmdata = lowpass(lmdata, 0.5, info.system.framerate); % LPF 2
  [lmdata, info] = resample_tts(lmdata, info, 1, 1e-5);
  % Block Average the measurement data
  badata = BlockAverage(lmdata, … info.paradigm.synchpts(info.paradigm.Pulse_2), dt);
  badata=bsxfun(@minus,badata,mean(badata,2));
Plots and images on right show differential measurements, computed as the logarithm of the ratio of each signal and its temporal average
Preprocessing comprises filters, processing, and averaging in order to reduce noise and physiologic components of the signals to highlight response to the stimulus
For a more in-depth exploration of pre-processing parameter settings, please see the Tutorial on Pre-processing.
After
Before
Block-averaged

## Slide 6: Reconstruction & Spectroscopy
DOT Acquisition
Log-mean
Detect noisy channels
Band-pass filter
Superficial signal regression
Resample
Low-pass filter
Reconstruction
Spectroscopy
Light
Model
Absorption image volumes are reconstructed from the processed measurements based on a regularized inversion of the A matrix (for details, see, e.g., Eggebrecht et al., Neuroimage, 2012)
  %% Reconstruct absorption, each wavelength
  if ~exist('A', 'var')
  load('A_AdultV24x28.mat') % Contains A-matrix, info.
  end
  for j = 1:2 % each wavelength
  keep = (info.pairs.WL == j) & (info.pairs.r2d <= 40) & info.MEAS.GI;
  % Invert A-Matrix
  iA = Tikhonov_invert_Amat(A(keep, :), 0.01, 0.1);
  % Smooth Inverted A-Matrix
  iA_smoothed = smooth_Amat(iA, dim, 3);
  % Reconstruct Image Volume
  cortex_mu_a(:, :, j) = reconstruct_img(preprocessed(keep, :), iA_smoothed);
  end
  Image volumes store estimated absorption values as voxels by time by wavelength.
  Hemoglobin images are computed from the wavelength-dependent absorption images
  %% Spectroscopy, convert to Hb
  load('E.mat')
  cortex_Hb = spectroscopy_img(cortex_mu_a, E);
  cortex_HbO = cortex_Hb(:, :, 1);
  cortex_HbR = cortex_Hb(:, :, 2);
  cortex_HbT = cortex_HbO + cortex_HbR;

## Slide 7: Spatial normalization and visualization
DOT Acquisition
Log-mean
Detect noisy channels
Band-pass filter
Superficial signal regression
Resample
Low-pass filter
Reconstruction
Spectroscopy
Spatial normalization
Light
Model
As in the full tutorial, the reconstructed images are visualized on a spatially registered anatomical background
  [MNI,infoB]=LoadVolumetricData('Segmented_MNI152nl_on_MNI111',[],'4dfp');
  MNI_dim = affine3d_img(MNI,infoB,A.info.tissue.dim,eye(4),'nearest');
  HbO_T1 = affine3d_img(cortex_HbO, A.info.tissue.dim, infoB, eye(4));
  Block average and visualize
  badata_HbO = BlockAverage(cortex_HbO,info.paradigm.synchpts(info.paradigm.Pulse_2), dt);
  badata_HbO=bsxfun(@minus,badata_HbO,badata_HbO(:,1));
  badata_HbOvol = Good_Vox2vol(badata_HbO,A.info.tissue.dim);
  Params.Scale=0.8*max(abs(badata_HbOvol(:)));
  Params.Th.P=0;
  Params.Th.N=-Params.Th.P;
  PlotSlicesTimeTrace(MNI_dim,A.info.tissue.dim,Params,badata_HbOvol,info)
  The results below show the reconstructed oxyhemoglobin (HbO) volume.

## Slide 8: Visualization of Absorption Volumes
Reconstructed absorption volumes at 750 and 850 nm show sensitivity of the 850 nm wavelength to HbO and 750 nm wavelength to HbR.
  Images are shown with a threshold of 20% of the maximum amplitude:
  Params.Scale=0.8*max(abs(badata_HbOvol(:)));
  Params.Th.P=0.2*Params.Scale;
  Params.Th.N=-Params.Th.P;
  Params.Cmap='jet';
  PlotSlicesTimeTrace(MNI_dim,A.info.tissue.dim,Params,badata_HbOvol,info)
HbO
- 750 nm
- 850 nm

## Slide 9: Hemoglobin volumes - HbO, HbR, HbT
  Oxy-, deoxy-, and total hemoglobin estimates can also be visualized
HbO
HbR
HbT

## Slide 10: Spatial Smoothing
Spatial smoothing is implemented with a 3-dimensional Gaussian filter. The third parameter dictates the degree of smoothing via the filter width, in voxels
  % Smooth Inverted A-Matrix
  iA_smoothed = smooth_Amat(iA, dim, 3);
  Increasing smoothing generally gives improved signal to noise ratio at the expense of resolution
HbO – Smoothed with 5 voxel filter
HbO – Smoothed with 3 voxel filter
HbO – Not smoothed

## Slide 11: Reconstruction Parameters
Reconstruction via regularized inversion is controlled by two parameters
  iA = Tikhonov_invert_Amat(A.A(keep, :), 0.01, 0.1); % Invert A-Matrix
  The first parameter controls a tradeoff between image resolution and noise, similar to spatial smoothing. The typical value for this parameter is
  The second parameter controls spatially variant regularization. A lower value increases reconstruction amplitude in low-sensitivity voxels, e.g., deeper voxels. Typical value is
HbO – ,
HbO – ,
HbO – , 05

## Slide 12: That’s It (For Now)
Congratulations! You have finished the NeuroDOT Tutorial for the full processing of CCW data acquired with the 24x28 visual pad.
See other Sample Results Appendices for example visualizations of these same processing steps on the other Sample Data included in the toolbox.
Also, see the PreProcessing and Reconstruction tutorials to gain a deeper understanding of the effects of altering the processing parameters.
For further questions or more information, please consult the NeuroDOT User Manual and the various Appendices.
NeuroDOT Team:
  Adam Eggebrecht (aeggebre@wustl.edu)
  Jason Trobaugh (jasont@wustl.edu)